## Slide 1: Domain of the work: Tool Condition Monitoring in Industrial Engineering using AI and Deep Learning Tentative Title : Machine Fault analysis and Tool condition monitoring
Batch- 5:
      211FA04009
      211FA04003
      211FA04452
      Guide:
      Dr. S V Phani Kumar

## Slide 2: Motivation :
During our project title research, we came across an interesting historical example from the Toyota Company before the 1950s.
Toyota faced numerous rejections from their testing team because many of their products were found to have faults.
After continuous rejections, they thoroughly investigated their production process and discovered that the root cause was tool wear in their machines.
Once they addressed this issue, they were able to improve their processes and small damage doesn't make any change in such big industries.
However, for small companies, even minor damages to output can lead to significant losses, as they may not have the resources or scale to absorb such setbacks.
To address this challenge, we decided to do this project to proactively monitor tool condition and surface quality. By implementing an intelligent tool condition monitoring system.

## Slide 3: Literature Survey
[1] Title: Assessment of Tool Condition and Surface Quality Using Hybrid Deep Neural Network: CNN-LSTM-Based Segmentation and Statistical Analysis
Author: K. Venkata Rao
This paper addresses tool wear prediction challenges in machining processes by leveraging a CNN-LSTM hybrid model that processes heterogeneous data, including tool images, vibration signals, and surface roughness. It builds on prior works that used CNNs for image-based wear detection and LSTMs for temporal data but combines these strengths for enhanced accuracy. The study incorporates YOLOv8 for efficient wear region segmentation, achieving mAP values above 0.9, and reports RMSE values as low as 0.018 mm for wear depth with R² up to 0.974 for wear length prediction. While advancing tool condition monitoring, it highlights gaps in integrating diverse data types and calls for optimized hybrid architectures for broader applications in machining.

## Slide 4
[2] Title: Tool Wear Condition Monitoring Method Based on Deep Learning with Force Signals
Author: Yaping Zhang et.al
The literature survey in this paper highlights the challenges in tool wear condition monitoring due to nonlinear and time-varying machining processes. Traditional machine learning approaches, such as support vector machines and random forests, are limited by shallow feature extraction and inefficiency. Recent advances integrate deep learning models with industrial data to improve generalization and accuracy. Techniques like wavelet transforms, Fourier transforms, and Gramian angular fields have been employed to transform sensor signals into images, enabling improved classification. Compared to methods like ResNet (62.9% accuracy) and AlexNet (70.1% accuracy), convolutional neural networks with multiscale features achieve accuracy above 90%, offering superior precision, recall, and robustness. These developments address data imbalance and enhance real-time monitoring capabilities.

## Slide 5
[3] Title: Milling Tool Wear Prediction Method Based on Deep Learning Under Variable Working Conditions
Authors: MINGWEI WANG et.al
This paper investigates deep learning methods for predicting milling tool wear under variable working conditions. Traditional machine learning approaches struggled with high-dimensional, non-stationary data and complex relationships between tool wear and working conditions. This study employs a stacked autoencoder for adaptive feature extraction and an LSTM network to model time-series correlations. By integrating fused machining signals and working condition factors into a unified framework, the proposed method improves prediction accuracy. Experimental validation using public datasets demonstrates its reliability and efficiency, highlighting its potential for real-time applications in tool wear monitoring.

## Slide 6
[4] Title: Tool Condition Monitoring With Multiscale Discriminant Sparse Decomposition
Authors: Kunpeng Zhu,Xin Lin
This paper focuses on Tool Condition Monitoring (TCM), a crucial aspect of manufacturing, aimed at detecting tool conditions such as wear, chipping, or breakage in real time. It integrates advanced signal processing and machine learning techniques for accurate and efficient monitoring.The system uses Wavelet Packet Decomposition (WPD) to preprocess signals by breaking them into frequency components, extracting meaningful features. Sparse Representation then efficiently encodes these features by representing them as a combination of a few essential dictionary atoms, reducing noise and focusing on relevant information. Next, Discriminative Dictionary Learning trains a dictionary optimized for distinguishing tool conditions, employing Fisher’s Discriminant Analysis (FDA) to enhance class separability. Finally, the system uses the Fisher Discriminant Ratio (FDR) for classification, assigning the signal to the appropriate tool condition.

## Slide 7: About Dataset:
The dataset consists of 27 records each with 25 features and was split into 70%, 20%, and 10% for training, validation, and test, respectively
Material Studied: AISI D2 Steel, machined using a cemented carbide mill cutter.
Dataset consists of Heterogeneous data combining:
  Tool Images: Annotated flank wear images using Roboflow for wear segmentation.
  Vibration Signals: Processed using Fast Fourier Transform (FFT), with 18 features extracted (time and frequency domains).
  Machining Properties: Includes spindle speed, feed/tooth, machining length, wear length, wear depth, and surface roughness.

## Slide 8
Working Condition – (3 features):
Spindle speed, Feed, Machining length
Time domain- (13 features):
Standard deviation, minimum value, maximum value, average value, amplitude factor, peak-to-peak value, skewness, root mean square, kurtosis, Energy, impact factor, waveform factor, and margin factor
Frequency domain –(5 features):
frequency domain amplitude average, variance frequency, frequency variance, mean square frequency and center of gravity frequency
After segmentation- (3 features):
Wear tool identification image, Wear length, Wear depth
Profilometer- (1 feature):
Surface roughness

## Slide 9: Objectives:
To develop an efficient system for tool condition monitoring using heterogeneous data and advanced image processing techniques like SAM for accurate detection, and prediction of tool wear and surface quality.

## Slide 10: Work flow and Timeline:

## Slide 11
Workflow | Timeline
Title and base paper selection | 1st week of Jan
Data Acquisition | 1st Week of Jan
Image Segmenation | Jan month end
Implementation of Base model | 2nd Week of Feb
Implementation of Proposedmodel | 1st week of March
Experimentation results | 2nd week of March
Theisis drafting | 1st Week of April

## Slide 12: Conclusion:
In conclusion, the development of an intelligent tool condition monitoring system combined with real-time surface quality analysis addresses critical challenges faced by small-scale manufacturing industries. By drawing inspiration from historical instances like Toyota's tool wear issues before the 1950s, we have aimed to create a system that proactively monitors tool health and surface quality. This approach ensures that even minor damages or wear in tools do not lead to significant losses, which is crucial for small companies that lack the resources to absorb such setbacks.

## Slide 13: References:
[1] Rao, K.. (2024). Assessment of Tool Condition and Surface Quality Using Hybrid Deep Neural Network: CNN-LSTM-Based Segmentation and Statistical Analysis. Journal of Tribology. 147. 1-33. 10.1115/1.4067496
[2] Zhang, Y., Qi, X., Wang, T., & He, Y. (2023). Tool wear condition monitoring method based on deep learning with force signals. Sensors, 23(10), 4595.
[3] Wang, M., Zhou, J., Gao, J., Li, Z., & Li, E. (2020). Milling tool wear prediction method based on deep learning under variable working conditions. IEEE Access, 8, 140726-140735.
[4] K. Zhu and X. Lin, "Tool Condition Monitoring With Multiscale Discriminant Sparse Decomposition," in IEEE Transactions on Industrial Informatics, vol. 15, no. 5, pp. 2819-2827, May 2019, doi: 10.1109/TII.2018.2867451.